## Slide 1
AFSIM Developer Training
9 – Communications
AFRL/RQQD

## Slide 2: Acronyms and Definitions
AFSIM - Advanced Framework for Simulation, Integration, and Modeling
AGL – Above Ground Level
DIS – Distributed Interactive Simulation
DTED – Digital Terrain Elevation Data
EO/IR – Electro-Optical/Infra-Red
ESM – Electronic Support Measure
FOV – Field Of View
GUI – Graphical User Interface
HLA – High Level Architecture
IEEE – Institute of Electrical & Electronics Engineers, Inc.
JTIDS – Joint Tactical Information Distribution System
MSL – Mean Sea Level
PDU – Protocol Data Unit
RCS – Radar Cross Section
SAM – Surface-to-Air Missile
SAR – Synthetic Aperture Radar
VESPA – Visual Environment for Scenario Preparation and Analysis
WKF – Warlock Framework
WSF – World Simulation Framework
dB - decibels
dBsm – decibel square meters
deg – degrees
ft – feet
GHz– GigaHertz
kts – knots
m - meters
m^2 – square meters
mw – megawatts
nm – nautical miles
s – seconds

## Slide 3: Introduction
This lab demonstrates how to create a new AFSIM communication device and a new AFSIM message
Additionally, the Distributed Interactive Simulation (DIS) interface will be used to send the new message using a DIS Signal Protocol Data Unit (PDU)
An AFSIM communication device is a platform component that provides the means to send messages (WsfMessage) between platforms
The following exercise provides practice working with AFSIM communications
  Exercise 1: Registering a default Application Extension, a new Scenario Extension, and a new Simulation Extension
  Exercise 2: Implementing ProcessInput for the communication’s scenario
  Exercise 2: Creating a custom AFSIM communication device and message
  Exercise 3: Creating a custom AFSIM Communications script interface

## Slide 4: Problem Statement
Create a new communication device type called SIGNAL_COMM and a new message class called LocationMessage
The SIGNAL_COMM should:
  Be able to send all the core message types including the new LocationMessage
  Whenever a new LocationMessage is sent by the SIGNAL_COMM device, the message will also be sent over the DIS interface using a Signal PDU containing the contents of the LocationMessage
    Other DIS-enabled simulations can read Location Messages
References:
AFSIM Developers Web-based data.
AFSIM Source Codes and Visual Studio search functions.
AFSIM Documentation.

## Slide 5: Learning Objectives
You gain hands-on knowledge about:
  Creating new types of communication devices and messages
  Implementing the send and receive methods for a new communication device
  Packing and unpacking a DIS Signal PDU with custom data
  Reinforce your skills with creating a default application extension and a plugin
    The new script types are registered by the scenario extension
  Reinforce your skill with creating a simulation extension and a scenario extension
  Understand how to extend existing script classes to include new methods, without modifying core code

## Slide 6: Prerequisites
Before working on this lab, you should:
  Be familiar with Wizard and the AFSIM scripting Language
    AFSIM analyst course or equivalent experience is recommended
  Have available and be familiar with using Microsoft® Visual Studio 2017® or newer to compile an application
  Be familiar with using Microsoft Windows® Explorer
  Have the latest version of Mystic installed
Mystic is an interactive software environment for analyzing AFSIM results.

## Slide 7: Communications in the AFSIM Framework
AFSIM includes a robust set of communication and message options within the basic framework
Using the C++ architecture, developers can extend classes to create new communication devices and new messages
AFSIM Framework
Infrastructure
Components
Platform Components
Scenario Management
Time Management
Interface
Event Management
Distributed Simulation Interfaces
Script
Geospatial Data Management
Simulation Management
Event Management
Extensions
Observers
Movers
Sensors
Weapons
Communications
Processors
Other Platform
Components
Scenario Management
Time Management
Geospatial Data Management
Distributed Simulation Interfaces
Scripting
Language
Utilities
Extensions
Observers
Sensor
Components
Weapon
Components
Processor
Components
Comm
Components
Plug-in
Management
Non-Platform
Components

## Slide 8: Comm Exercise Extends WsfComm Class
Add a new SignalComm class to AFSIM.
SignalComm

## Slide 9: Detailed AFSIM Comm Classes

## Slide 10: Detailed AFSIM Comm Classes

## Slide 11: Comm Exercise Extends WsfMessage
Add a new LocationMessage class to AFSIM
LocationMessage

## Slide 12: AFSIM Plugins & Extensions
AFSIM extensions must derive from WsfExtension:
    WsfScenarioExtension – extensions that will provide new scenario commands (requiring a new ProcessInput for those commands) will need to inherit this class
    WsfSimulationExtension – extensions that will access the simulation will need to inherit this class
    WsfApplicationExtension – extensions that will create new script types, or will utilize a simulation extension or scenario extension, will need to inherit this class
WsfExtension
WsfSimulationExtension
WsfScenarioExtension
WsfApplicationExtension
WsfDefaultApplicationExtension
WsfScenario
WsfSimulation
WsfApplication
WsfStandardApplication
CommLab::Interface
SignalCommRegistration

## Slide 13: New Input Parameters
Code modifications are needed to accept:
  Keyword source_track_number_offset with an input value
Existing AFSIM methods will be used to set other comm input values
  Example input:
comm comm-net SIGNAL_COMM
source_track_number 100
end_comm

## Slide 14: Comm Scenario
Inspect the comm_types.txt file and observe the following:
  The platform_type called COMM_PLATFORM carries the SIGNAL_COMM (BLUE_COMM) communication device
comm BLUE_COMM SIGNAL_COMM
debug
end_comm
platform_type COMM_PLATFORM WSF_PLATFORM
comm comm-net BLUE_COMM
internal_link msg_processor
end_comm
processor msg_processor WSF_SCRIPT_PROCESSOR
end_processor
end_platform_type
COMM_PLATFORM
SIGNAL_COMM
BLUE_COMM

## Slide 15: Comm Scenario
Inspect the comm_scenario1.txt file and observe the following:
  The blue_commander platform sends out a WsfControlMessage every 5 seconds to all subordinates
platform blue_commander CMDR
side blue
commander SELF
position 39:39:12n 123:08:00w altitude 0 ft agl
execute at_interval_of 5 s
WsfControlMessage cntrlMsg = WsfControlMessage();
cntrlMsg.SetFunction("I COMMAND YOU");
PLATFORM.Comm("comm-net").SendMessageToSubordinates("", cntrlMsg);
end_execute
end_platform
File: comm_scenario1.txt

## Slide 16: Comm Scenario
File: comm_scenario1.txt
Inspect the comm_scenario1.txt file and observe the following:
  The blue_commander platform has an on_message block to write a message when a LOCATION_MESSAGE is received from his subordinates
platform blue_commander CMDR
side blue
commander SELF
position 39:39:12n 123:08:00w altitude 0 ft agl
execute at_interval_of 5 s
WsfControlMessage cntrlMsg = WsfControlMessage();
cntrlMsg.SetFunction("I COMMAND YOU");
PLATFORM.Comm("comm-net").SendMessageToSubordinates("", cntrlMsg);
end_execute
end_platform
platform_type CMDR COMM_PLATFORM
icon cmd_post
edit processor msg_processor
// --- * --- * ---
script void ProcessMessage(LocationMessage aMsg)
writeln("Message received of type: ", aMsg.Type());
writeln("Received a Location Message from ", aMsg.Originator());
end_script
on_message type LOCATION_MESSAGE
script
ProcessMessage((LocationMessage) MESSAGE);
end_script
end_on_message
File: comm_types.txt

## Slide 17: Comm Scenario
platform blue-3 AIRCRAFT
side blue
position 38:28:47.764n 122:50:13.166w altitude 30000 ft agl
end_platform
Inspect the comm_scenario1.txt file and observe the following:
  The blue-1, blue-2, and blue-3 platforms send out a LocationMessage every 5 seconds to commander
File: comm_scenario1.txt
platform_type SUBORDINATE COMM_PLATFORM
execute at_interval_of 5 s
// Send location
LocationMessage msg = LocationMessage();
PLATFORM.Comm("comm-net“).SendMessageToCommander(msg);
end_execute
end_platform_type
platform_type AIRCRAFT SUBORDINATE
icon fighter
mover WSF_AIR_MOVER
end_mover
end_platform_type
File: comm_types.txt
platform blue-1 AIRCRAFT
side blue
commander blue_commander
route
end_platform
platform blue-2 AIRCRAFT
side blue
commander blue_commander
route
end_platform

## Slide 18: Comm Scenario
Inspect the comm_scenario1.txt file and observe the following:
  These platforms have an on_message block to respond to a WsfControlMessage
platform blue-1 AIRCRAFT
side blue
commander blue_commander
route
end_platform
File: comm_scenario1.txt
platform blue-2 AIRCRAFT
side blue
commander blue_commander
route
end_platform
platform blue-3 AIRCRAFT
side blue
position 38:28:47.764n 122:50:13.166w altitude 30000 ft agl
end_platform
platform_type SUBORDINATE COMM_PLATFORM
edit processor msg_processor
// --- * --- * ---
script void ProcessMessage(WsfControlMessage aMsg)
// Send status
WsfStatusMessage statusMsg = WsfStatusMessage();
statusMsg.SetStatus("OK");
PLATFORM.Comm("comm-net").SendMessageToCommander("",
statusMsg);
end_script
on_message
type WSF_CONTROL_MESSAGE
script ProcessMessage((WsfControlMessage) MESSAGE);
end_script
end_on_message
end_processor
File: comm_types.txt

## Slide 19: Messages Generated
“I COMMAND YOU” control messages
  are sent out every 5 sec.
  are only sent to subordinates
    platforms that have commander blue_commander (blue-1 & blue-2)
  “OK” control messages are immediately sent back to the commander
blue_commander
blue_1
blue_2
blue_3
WSF_CONTROL_MESSAGE
“I COMMAND YOU”
WSF_CONTROL_MESSAGE
“I COMMAND YOU”
WSF_CONTROL_MESSAGE
“OK”
isr_1
WSF_CONTROL_MESSAGE
“OK”
Simulation instance 1
(running comm_scenario1.txt)
Simulation instance 2
(running comm_scenario2.txt)

## Slide 20: Comm Scenario
Inspect the comm_scenario2.txt file
  A platform ISR-1 receives SIGNAL_COMM messages from platforms in comm_scenario1 and uses WsfDraw to display these locations as icons in Mystic
    Although we demonstrate this in an AFSIM simulation, another simulation could also receive and, decode, and display these locations
platform isr-1 COMM_PLATFORM
add processor internal_generation msg_processor
update_interval 5.0 seconds
internal_link msg_processor
on_update
// Send location
LocationMessage msg = LocationMessage();
SendMessage(msg);
end_on_update
end_processor
File: comm_scenario2.txt

## Slide 21: Comm Scenario
Inspect the comm_scenario2.txt file
  ISR-1 also demonstrates sending a location message over internal links for display with WsfDraw
platform isr-1 COMM_PLATFORM
edit processor msg_processor
on_message type LOCATION_MESSAGE
script
LocationMessage msg = (LocationMessage)MESSAGE;
WsfDraw draw = WsfDraw();
draw.Erase(msg.SourceTrackNumber());
draw.SetId(msg.SourceTrackNumber());
draw.SetDuration(20.0);
draw.End();
end_script
end_on_message
end_processor
File: comm_scenario2.txt

## Slide 22: Messages Generated
Location messages
  are sent out every 5 sec.
  are only sent to platform’s commander
    blue-1 sends to blue_commander
    blue-2 sends to blue_commander
    blue-3 sends messages, but they go to nobody (no commander)
    isr-1 sends messages, but they go to nobody(no commander)
  isr-1 scans comm-net for ALL Location messages
    For each one received, it draws the platform at that location
blue_commander
blue_1
blue_2
blue_3
LOCATION_MESSAGE
(lat, lon, alt, course, speed)
isr_1
LOCATION_MESSAGE
(lat, lon, alt, course, speed)
LOCATION_MESSAGE
(lat, lon, alt, course, speed)
???
LOCATION_MESSAGE
(lat, lon, alt, course, speed)
???
Simulation instance 2
(running comm_scenario2.txt)
Simulation instance 1
(running comm_scenario1.txt)

## Slide 23: Comm Scenario
isr-1
T = 0
Queued message for transmission.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.2; size 0)
Scheduled transmission event.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.2; size 0)
Queued message for transmission.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.3; size 0)
Scheduled transmission event.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.3; size 0)
Comm has started transmission of message.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.2; size 0)
Message transmission completed.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.2; size 0)
Comm has started transmission of message.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.3; size 0)
Message transmission completed.
T = 2.96422
Comm: blue_commander.comm-net
Message: 35 (dest 0.1.0.3; size 0)
Comm receiving message.
T = 2.96464
Comm: blue-1.comm-net
Message: 35 (dest 0.1.0.2; size 0)
blue_commander
blue_1
blue_2
blue_3

## Slide 24: Getting Started (1/3)
Open CMake GUI
Check BUILD_WITH_comm_exercise
Press “Configure”
  (Respond to any prompts asking for a compiler)
Press “Generate”

## Slide 25: Getting Started (2/3)
If Visual Studio is already open:
  Navigate to it and select Reload All when prompted.
Alternatively, open the solution file afsim.sln by:
  Opening from swdev\build
  Clicking “Open Project” from CMake

## Slide 26: Getting Started (3/3)
This project uses the following 12 source files:
  CommPluginRegistration.cpp
  DataLinkMessage.hpp
  DataLinkMessage.cpp
  DataLinkLocationMessage.hpp
  DataLinkLocationMessage.cpp
  Interface.hpp
  Interface.cpp
  LocationMessage.hpp
  LocationMessage.cpp
  SignalComm.hpp
  SignalComm.cpp
  SignalCommRegistration.hpp
Note that many solutions are possible; we have provided a solution in order to complete our training exercise in a short time period.

## Slide 27: Classes Utilized by this Exercise
This exercise utilizes the following classes:
  class DataLink::Message
    Defines a “Link Layer” message header
    Lives in namespace DataLink
  class DataLink::LocationMessage : public DataLink::Message
    Defines a “Link Layer” message to encode the elements of a LocationMessage (see below)
    The inherited DataLink::Message incorporates a header into the message
    Lives in namespace DataLink
  class WsfControlMessage : public WsfMessage
    Utilized by our scenario scripts
    Allows commanders (those with subordinates) to send out “I CONTROL YOU” messages
    Already defined in the core script interface
  class WsfStatusMessage : public WsfMessage
    Utilized by our scenario scripts
    Allows subordinates (those platforms with a commander) to respond with “OK” messages
    Already defined in the core script interface
  class LocationMessage : public WsfMessage
    Creates a new type of high level message to encode a platform’s location data

## Slide 28: Classes Utilized by this Exercise
This exercise utilizes the following classes:
  class ScriptLocationMessageClass : public WsfScriptMessageClass
    Declares and Defines the new script methods which will be available to the scenario definition for sending and receiving the new LocationMessage(s)
  class SignalComm : public wsf::comm::Comm
    Defines a Comm device that triggers the sending / receiving of DIS signal PDUs which encode messages
  class CommLab::Interface : public WsfSimulationExtension
    Primarily servers as an interface to the DIS communications protocol for sending and receiving messages
    Lives in namespace CommLab
  class SignalCommRegistration : public WsfScenarioExtension
    Defines three methods:
      AddedToScenario: adds the new SignalComm comm type to the scenario
      Adds the new ScriptLocationMessageClass to the application’s script types
      ProcessInput: simply invokes the CommLab::Interface::ProcessInput to handle scenario commands
      SimulationCrated: registers the CommLab::Interface simulation extension with the simulation
  class WsfDefaultApplicationExtension : public WsfApplicationExtention
    a simple application extension with a ScenarioCreated method
    Templated on a scenario extension
    When ScenarioCreated is invoked, it registers the scenario extension with the scenario

## Slide 29: Communications Exercises
Exercise 1
  Complete registration of a default application extension, with a scenario extension
Exercise 2
  Complete scenario extension ProcessInput and Interface::ProcessInput
Exercise 3
  Understand, and complete the implementation of class methods that handle sending, receiving, and processing messages
Exercise 4
  Understand and complete code for new script methods

## Slide 30: Exercise 1
Complete registration of a default application extension, which is templated upon a scenario extension

## Slide 31: AFSIM Plugins & Extensions
All AFSIM extensions must derive from WsfExtension:
  Three predefined extension classes already exist (can be inherited from)
    WsfScenarioExtension – extensions that will provide new scenario commands (requiring a new ProcessInput for those commands) will need to inherit this class
    WsfSimulationExtension – extensions that will access the simulation will need to inherit this class
    WsfApplicationExtension – extensions that will create new script types, or will utilize a simulation extension or scenario extension, will need to inherit this class
WsfExtension
WsfSimulationExtension
WsfScenarioExtension
WsfApplicationExtension
WsfScenario
WsfSimulation
WsfApplication
WsfStandardApplication
Main application classes used
in mission/warlock

## Slide 32: AFSIM Plugins & Extensions
All AFSIM extensions must derive from WsfExtension:
  Three predefined extension classes already exist (can be inherited from)
    WsfScenarioExtension – extensions that will provide new scenario commands (requiring a new ProcessInput for those commands) will need to inherit this class
    WsfSimulationExtension – extensions that will access the simulation will need to inherit this class
    WsfApplicationExtension – extensions that will create new script types, or will utilize a simulation extension or scenario extension, will need to inherit this class
WsfExtension
WsfSimulationExtension
WsfScenarioExtension
WsfApplicationExtension
WsfScenario
WsfSimulation
WsfApplication
WsfStandardApplication
Main application classes used
in mission/warlock
Sets up the new Application
Extension classes to work
with AFSIM
Sets up the new ScenarioExtension classes to work
with AFSIM
WsfDefaultApplicationExtension
CommLab::Interface
SignalCommRegistration
Sets up the new SimulationExtension classes to work
with AFSIM

## Slide 33: Extensions
Applications, Scenarios, and Simulations can all be “Extended”
  Application Extensions are owned by the Application
    Represent optional capabilities that can be added to an application.
    Used if you need new script types (sensors, weapons, components, movers)
    This is the entry point to registering all extensions in AFSIM
    An application extension is required if you are going to create a scenario extension or a simulation extension
  We need a new plugin because we need to register the default application extension
    see the file CommPluginRegistration.cpp

## Slide 34: Comm Exercise 1 — Review 1 CommPluginRegistration.cpp
In CommPluginRegistration.cpp, review WsfPluginVersion
extern "C"
{
COMM_EXERCISE_EXPORT void WsfPluginVersion(UtPluginVersion& aVerrsion)
{
aVersion = UtPluginVersion(WSF_PLUGIN_API_MAJOR_VERSION,
WSF_PLUGIN_API_MINOR_VERSION,
WSF_PLUGIN_API_COMPILER_STRING);
}
}

## Slide 35: Comm Exercise 1 — Task 1
Complete WsfPluginSetup
  Invoke aApplication.RegisterExtension
  The first argument should be the name of the application extenstion, which is “signal_comm_registration”
  The second argument should be a newly created unique_ptr to a WsfDefaultApplicationExtension templated on our scenario extension SignalCommRegistration

## Slide 36: Comm Exercise 1 — Task 1 Solution CommPluginRegistration.cpp
extern "C"
{
COMM_EXERCISE_EXPORT void WsfPluginVersion(UtPluginVersion& aVerrsion)
{
aVersion = UtPluginVersion(WSF_PLUGIN_API_MAJOR_VERSION,
WSF_PLUGIN_API_MINOR_VERSION,
WSF_PLUGIN_API_COMPILER_STRING);
}
COMM_EXERCISE_EXPORT void WsfPluginSetup(WsfApplication& aApplication)
{
// EXERCISE 1 TASK 1
// Invoke aApplication’s RegiserExtension method
// The first argument is the name of the application extension
// The second argument is a newly created unique_ptr to a default application extension
// that is templated upon a scenario extension (the SignalCommRegisration class)
aApplication.RegisterExtension("signal_comm_registration",
ut::make_unique<WsfDefaultApplicationExtension<SignalCommRegistration>>());
}
}
Note: when we register the application extension WsfDefaultApplicationExtension, we are also registering the SignalCommRegistration scenario extension

## Slide 37: Application Extensions
To extend an Application, you must create a class that inherits class WsfApplicationExtension
class myAppExtension: public WsfApplicationExtension { … }
  You should override the following members:
    AddedToApplication: to receive notification that extension was added to the application – often used to register additional script class and methods, etc.
    ScenarioCreated: called at end of Scenario constructor in order to receive notification from the application that the scenario was created – useful to register an Scenario extension if needed
    SimulationCreated: called from the Simulation’s Initialize method in order to receive notification from the application that the simulation was created – useful to register an Simulation extension if needed
    ProcessCommandLine: called from WsfApplication::ProcessCommandLine method to examine current argument and process it if necessary
    PrintGrammar: prints out the extended grammar recognized by the extension
    ProcessCommandLineCommands: called by WsfApplication’s ProcessCommandLineCommands to allow the extension to process/handle any commands it needs to recognize

## Slide 38: Application Extensions
To extend an Application, you must create a class that inherits class WsfApplicationExtension
  We will use WsfDefaultApplicationExtension which will register the scenario extension
class WsfDefaultApplicationExtension: public WsfApplicationExtension { … }
  This class overrides the following members for an ApplicationExtension:
    ScenarioCreated: called at end of Scenario constructor in order to receive notification from the application that the scenario was created – useful to register a Scenario extension if needed
  This class is templated on a WsfScenarioExtension (SignalCommRegistration is derived from this class)
  When the WsfDefaultApplicationExtension::ScenarioCreated method is executed by the WsfScenaro constructor, it performs the registration of the SignalCommRegistration scenario extension with the scenario

## Slide 39: Scenario Extensions
Scenarios can all be “Extended” as well
  Scenario Extensions are owned by the Scenario
    Represent optional types that can be added to a scenario.
    Used if you need new types (components, observers, comms)
    An application extension is required if you are going to create a scenario extension (or a simulation extension – covered later)
  We also need an scenario extension if
    We are creating simulation level commands

## Slide 40: Scenario Extensions
To extend a Scenario, you must create a class that inherits class WsfScenarioExtension
class myScenarioExtension: public WsfScenarioExtension
  You can override:
    AddedToScenario: to receive notification that extension was added to the scenario – often used to register additional component type objects and factories
    ProcessInput: processes any scenario input commands that must be recognized by the extension
    FileLoaded: notifies extension that a file has been loaded into the scenario
    Complete: called from WsfScenario::LoadComplete – notifies extension that all scenario input has been processed
    Complete2: called after all extensions have had their Complete method invoked
    SimulationCreated: called from WsfSimulation::Initialize – useful if a scenario extension needs an associated simulation extension – this method can register the simulation extension
    AlwaysCreate: determines if the extension is optional or required

## Slide 41: Observer Exercise Scenario Extension
To extend a Scenario, you must create a class that inherits class WsfScenarioExtension
class SignalCommRegistration: public WsfScenarioExtension
  We will override:
    AddedToScenario: to receive notification that extension was added to the scenario – often used to register additional component type objects and factories
    SimulationCreated: called from WsfSimulation::Initialize – useful if a scenario extension needs an associated simulation extension – this method can register the simulation extension
    ProcessInput: processes any scenario input commands that must be recognized by the extension

## Slide 42: Comm Exercise 1 — Review 2
Look at the definition of SignalCommRegistration::AddedToScenario
  Note that AddedToScenario is is executed by WsfScenarioExtension::RegisterExtension to notify the extension that it can now do things that require the scenario to exist, such as register new types, etc.
  AddedToScenario does the following:
    registers the new SignalComm comm type with the scenario
    Registers the new script type ScriptLocationMessageClass with the scenario

## Slide 43: Comm Exercise 1 — Review 2 SignalCommRegistration.hpp
class SignalCommRegistration : public WsfScenarioExtension
{
public:
...
void AddedToScenario() override
{
// Add the new comm type.
auto signalCommPtr = ut::make_unique<wsf::comm::SignalComm>(GetScenario());
GetScenario().GetCommTypes().Add(wsf::comm::SignalComm::GetSignalCommClassId(), std::move(signalCommPtr));
// Add the script classes to the script manager
GetScenario().GetApplication().GetScriptTypes()->Register(ut::make_unique<ScriptLocationMessageClass> ("LocationMessage", GetScenario().GetApplication().GetScriptTypes()));
}
...
};

## Slide 44: Comm Exercise 1 — Review 3
Note the member variable mPrototypeInterface is a CommLab::Interface simulation extension object
  mPrototypeInterface is a prototype simulation extension which is used when then scenario is reading the input files
    This object exists at the time that ProcessInput is called by the scenario, whereas the unique_ptr to a newly created simulation extension (created in SimulationCreated) does not exist yet
  When the simulation is created, a unique pointer to newly instantiated CommLab::Interface is created, and the members of mPrototypeInterface are copied over to it

## Slide 45: Comm Exercise 1 — Review 3 SignalCommRegistration.hpp
class SignalCommRegistration : public WsfScenarioExtension
{
public:
...
void SimulationCreated(WsfSimulation& aSim) override
{
// create a new CommLab::Interface simulation extension
auto InterfacePtr = ut::make_unique<CommLab::Interface>();
// use the prototype to initialize member variables in the new Interface
// have to copy members, since ProcessInput was already called on mPrototypeInterface
// only have to copy two members, since the others are not yet changed from default
InterfacePtr->SetDebugEnabled(mPrototypeInterface.GetDebugEnabled());
InterfacePtr->SetPrintMessages(mPrototypeInterface.GetPrintMessages());
// register the new extension
aSim.RegisterExtension("comm_lab_interface", std::move(InterfacePtr));
}
private:
CommLab::Interface mPrototypeInterface;
};

## Slide 46: Extensions
Simulations can all be “Extended” as well
  Simulation Extensions are owned by the Simulation
    Allow access to the simulation features.
    Used if you need access to the simulation itself(observers, comms, xio)
    An application extension is required if you are going to create a simulation extension (and you may need a scenario extension as well)
  We need a simulation extension if
    We need to know when platforms are added or deleted, and when sensor tracks are initialized or updated

## Slide 47: Simulation Extensions
To extend a Simulation, you must create a class that inherits class WsfScenarioExtension
class mySimulationExtension: public WsfSimulationExtension
  You must override:
    AddedToSimulation: called from WsfSimulation::RegisterExtension
    Initialize: called form WsfSimulation::Initialize – useful to perform extension initialization
    PrepareExtension: called from WsfSimulation::Initialize (called when a simulation is initialized) and from WsfSimulation::PrepareSimulation (called when a simulation is reloaded)
    PendingStart: simulation has just entered pending start state, allows extension to add additional platforms or other entities
    Start: called from WsfSimulation::Start – another opportunity to add additional platforms or other entities
    Complete: called from WsfSimulation::Complete – allows extension to release resources (files, sockets, etc.) that were allocated by Initialize or PrepareExtension

## Slide 48: Simulation Extensions
To extend a Simulation, you must create a class that inherits class WsfScenarioExtension
class Interface: public WsfSimulationExtension
  You must override:
    Initialize: called form WsfSimulation::Initialize – useful to perform extension initialization
    Start: called form WsfSimulation::Initialize – useful to inform extensions that the simulation is starting

## Slide 49: AFSIM Plugins & Extensions AFSIM mission startup sequence
Note: SignalCommRegistration contains
a member variable
mPrototypeInterface
which is a Comm::Interface
WsfStandardApplication: app
mission::main()
WsfStandardApplication::WsfStandardApplication()
CommPluginRegistration.cpp:WsfPluginSetup()
RegisterExtension(“signal_comm_registration”, ut::make_unique<WsfDefaultApplicationExtension<SignalCommRegistration>>())
WsfPluginSetup()
The WsfStandardApplication constructor utilizes the plugin manager to find and load all plugins (including those in the training folders -- because of the cmake option WSF_ADD_EXTENSION_PATH)
For each plugin found, executes WsfPluginSetup (note: this causes our communication exercise plugin’s WsfPluginSetup function to execute)
  This causes our comm exercise’s WsfDefaultApplicationExtension to be created and registered with app
First, mission creates a WsfStandardApplication named app
AddedToApplication()
  RegisterExtension then invokes the WsfApplicationExtension::AddedToApplication()
Note: WsfDefaultApplicationExtension does not override AddedToApplication, so this notification is essentially ignored
unique_ptr<WsfDefaultApplicationExtension<SignalCommRegistration>>
mPrototypeInterface

## Slide 50: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission then registers all of the necessary predefined extensions with app
WsfStandardApplication: app
mission::main()
RegisterExtension(…)
RegisterExtension(…)
RegisterExtension(…)
unique_ptr<WsfDefaultApplicationExtension<…>>

## Slide 51: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission then creates the scenario and invokes the WsfScenario constructor: WsfScenario scenario(app);
  This constructor invokes the WsfApplication::ScenarioCreated method
  This, in turn, invokes ScenarioCreated for all registered application extensions (including WsfDefaultApplicationExtension::ScenarioCreated)
    This, in turn, creates the SignalCommRegistration, and registers it with scenario
      RegisterExtension then invokes SignalCommRegistration::AddedToScenario
WsfStandardApplication: app
mission::main()
WsfScenario::WsfScenario(app)
ScenarioCreated(…)
ScenarioCreated(…)
WsfScenario: scenario
unique_ptr<SignalCommRegistration>
unique_ptr<WsfDefaultApplicationExtension<…>>
scenario.RegisterExtension(“signal_comm_registration”,
ut::make_unique<SignalCommRegistration>())
This is not the actual line of code executed, but this is what that code is equivalent to
AddedToApplication(…)
SignalCommRegistration::AddedToScenario registers the ScriptLocationMessageClass class with the script types manager

## Slide 52: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission invokes app.WsfStandardApplication::ProcessInputFiles()
which invokes WsfScenario::LoadFromFile()
  For each command in input,
    Invoke each of the core classes’ ProcessInput() methods
    Invoke each registered scenario extension’s ProcessInput()
      Invokes SignalCommRegistration::ProcessInput()
        Invokes the CommLab::Interface::ProcessInput()
WsfStandardApplication: app
mission::main()
WsfStandardApplication::ProcessInputFiles()
WsfScenario::LoadFromFile(…)
ProcessInput(…)
WsfScenario: scenario
unique_ptr<WsfDefaultApplicationExtension<…>>
ProcessInput(…)
unique_ptr<SignalCommRegistration>

## Slide 53: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission invokes app.WsfStandardApplication::ProcessInputFiles()
which, invokes WsfScenario::LoadFromFile()
and then invokes WsfScenario::CompleteLoad()
  Invokes each scenario extension’s Complete()
  Then invokes each scenario extension’s Complete2()
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
WsfStandardApplication::ProcessInputFiles()
WsfScenario::LoadFromFile(…)
WsfScenario::CompleteLoad(…)
Complete(…)
Complete2(…)
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 54: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission creates the Simulation by executing:
std::unique_ptr<WsfSimulation> simPtr =
app.CreateSimulation(scenario, …);
CreateSimulation invokes the WsfSimulation object’s constructor (with scenario as argument)
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: simPtr
WsfStandardApplication::CreateSimulation()
WsfSimulation::WsfSimulation()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 55: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
(where aSimPtr simPtr.get() )
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 56: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
WsfSimulation::Initialize invokes: mScenario.SimulationCreated(*this)
(where mScenario scenario and *this *simPtr.get() )
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
WsfScenario::SimulationCreated()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 57: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
WsfSimulation::Initialize invokes: mScenario.SimulationCreated(*this)
SimulationCreated Invokes: GetApplication().SimulationCreated(aSimulation)
(where GetApplication() app and aSimulation *simPtr.get() )
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
WsfScenario::SimulationCreated()
WsfApplication::SimulationCreated()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 58: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
WsfSimulation::Initialize invokes: mScenario.SimulationCreated(*this)
SimulationCreated Invokes: GetApplication().SimulationCreated(aSimulation)
  For each application extension invoke SimulationCreated(aSimulation)
  (where aSimulation *simPtr.get() )
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
WsfScenario::SimulationCreated()
WsfApplication::SimulationCreated()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 59: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
SimulationCreated Invokes: GetApplication().SimulationCreated(aSimulation)
  For each application extension invoke SimulationCreated(aSimulation)
  This Invokes SignalCommRegistration::SimulationCreated(aSimulation)
  (where aSimulation *simPtr.get() )
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
WsfScenario::SimulationCreated()
WsfApplication::SimulationCreated()
SignalCommRegistration::SimulationCreated()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 60: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
SimulationCreated Invokes: GetApplication().SimulationCreated(aSimulation)
  For each application extension invoke SimulationCreated(aSimulation)
  This Invokes SignalCommRegistration::SimulationCreated(aSimulation)
  This Invokes aSimulation.RegisterExtension(ut::make_unqiue<CommLab::Interface>())
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
WsfScenario::SimulationCreated()
WsfApplication::SimulationCreated()
WsfSimulation::RegisterExtension()
(where aSimulation *simPtr.get()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>
SignalCommRegistration::SimulationCreated()

## Slide 61: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
Next, WsfSimulation::Initialize invokes:
  This notifies all registered event observers that the simulation is about to be initialized
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
Note: the Interfaced class does not override this method, hence we do nothing with the notification
WsfObserver::SimulationInitializing(this)
WsfObserver::SimulationInitializing()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 62: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
Next, WsfSimulation::Initialize invokes: Initialize() on all the simulation extensions
  This invokes CommLab::Interface::Initialize()
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
CommLab::Interface::Initialize()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 63: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission initializes the Simulation by executing:
  app.InitializeSimulation(simPtr.get())
InitializeSimulation invokes: aSimPtr->Initialize()
Next, WsfSimulation::Initialize adds all available platforms to the simulation’s platform list
Finally, WsfSimulation::Initialize sets the simulation state to cPENDING_START
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::InitializeSimulation()
WsfSimulation::Initialize()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 64: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission runs the Simulation by executing:
  app.RunEventLoop(simPtr.get(), options)
RunEventLoop invokes: aSimPtr->Start()
  WsfSimulation::Start
    For each simulation extension invoke Start()
      Invokes CommLab::Interface::Start()
        Sets up the low level DIS Interface for communications
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::RunEventLoop()
WsfSimulation::Start()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>
CommLab::Interface::Start()

## Slide 65: AFSIM Plugins & Extensions AFSIM mission startup sequence
Mission runs the Simulation by executing:
  app.RunEventLoop(simPtr.get(), options)
RunEventLoop invokes: aSimPtr->Start()
  Loop until simulation is done
      Execute: aSimPtr->AdvanceTime()
        Advances time to next event time
        Fires the simulation events scheduled for the next event time
WsfStandardApplication: app
mission::main()
WsfScenario: scenario
unique_ptr<WsfSimulation>: SimPtr
WsfStandardApplication::RunEventLoop()
WsfSimulation::Start()
unique_ptr<WsfDefaultApplicationExtension<…>>
unique_ptr<SignalCommRegistration>

## Slide 66: Exercise 2
Complete scenario extension SignalCommRegistration::ProcessInput
Complete Interface::ProcessInput
Review Interface simulation extension’s Initialize and Start methods

## Slide 67: Comm Exercise 2 — Task 1
Complete the SignalCommRegistration::ProcessInput method by calling the prototype CommLab::Interface’s ProcessInput method:
  Use the member variable mPrototypeInterface to invoke ProcessInput
  Be sure to return the result of the call to mPrototypeInterface’s ProcessInput to the caller of SignalCommRegistration::ProcessInput

## Slide 68: Comm Exercise 2 — Task 1 Solution SignalCommRegistration.hpp
class SignalCommRegistration : public WsfScenarioExtension
{
public:
SignalCommRegistration() = default;
bool ProcessInput(UtInput& aInput) override
{
// EXERCISE 2 TASK 1
//! Call the CommLab::Interface prototype's ProcessInput method.
return mPrototypeInterface.ProcessInput(aInput);
}
...
private:
CommLab::Interface mPrototypeInterface;
};

## Slide 69: Comm Exercise 2 — Review 1
Inspect the CommLab::Interface class to become familiar with the class methods and attributes.
  CommLab::Interface will be implemented as a WsfSimulationExtension
  The Initialize method is automatically called by the simulation
  ProcessInput is called by the scenario through the SignalCommRegistration object
  HandleSignalPDU method is a callback method
  The SendMessage method is called when a SignalComm communication device is sending a message

## Slide 70: Comm Exercise 2 — Review 1 Interface.hpp
class Interface : public WsfSimulationExtension
{
public:
//! Constructor
Interface();
//! Virtual destructor
~Interface() noexcept override = default;
bool Initialize() override;
bool ProcessInput(UtInput& aInput);
void Start() override;
void SendMessage(double aSimTime,
WsfPlatform* aSenderPlatformPtr,
int aSourceTrackNumberOffset,
const WsfMessage* aMessagePtr);
//! Determine if debugging is enabled.
bool DebugEnabled() const { return mDebugEnabled; }
using LocationMessageReceivedCallback = UtCallbackListN<void(double, DataLink::LocationMessage*)>;
static LocationMessageReceivedCallback LocationMessageReceived;
private:
void HandleSignalPDU(WsfDisInterface* aInterfacePtr, const WsfDisSignal& aPdu);
UtCallbackHolder mCallbacks;
WsfDisInterface* mDisPtr;
bool mDebugEnabled;
bool mPrintMessages;
};

## Slide 71: Comm Exercise 2 — Task 2
In Interface.cpp, complete CommLab::Interface::ProcessInput method
  Task 2a: Write an if statement that will check if the variable cmd contains the string “print_messages”, and if true, sets the member mPrintMessages to true.
  Task 2b: Write an else if statement that will check if the variable cmd contains the string debug, and if true, sets the member mDebugEnabled to true.

## Slide 72: Comm Exercise 2 — Task 2 Solution Interface.cpp
bool Interface::ProcessInput(UtInput& aInput)
{
bool myCommand = false;
std::string cmd;
if ("comm_lab_interface" == aInput.GetCommand())
{
myCommand = true;
UtInputBlock block(aInput);
while (block.ReadCommand(cmd))
{
// EXERCISE 2 TASK 2a
// Write if statement to check if cmd contains “print_messages” and if true,
// sets mPrintMessages to true
if (cmd == "print_messages")
{
mPrintMessages = true;
}
// EXERCISE 2 TASK 2b
// Write else if statement to check if cmd contains “debug” and if true,
// sets mDebug to true
else if (cmd == "debug")
{
mDebugEnabled = true;
}
else
{
throw UtInput::BadValue(aInput);
}
}
}
return myCommand;
}
Notes: In Interface::Start, we ask the simulation for the extension called “dis_interface”. This gives us a WsfSimulationExtension, which we cast to a WsfDisInterface.
In Interface::Initialize, we register for a callback. This callback gets triggered when a dis signal is received by the AFSIM Dis Interface. When this happens, we want to process it in Interface::HandleSignalPDU

## Slide 73: Comm Exercise 2 — Review 2
In Interface.cpp, inspect the CommLab::Interface::Initialize method and CommLab::Interface::Start method
  Note that Initialize adds a callback to HandleSignalPDU to the list of callbacks stored in mCallbacks
  Note that start sets the member mDisPtr to point to the WsfDisInterface simulation extension

## Slide 74: Comm Exercise 2 — Review 2 Interface.cpp
Review and understand:
bool Interface::Initialize()
{
mCallbacks += WsfObserver::DisSignalReceived(&GetSimulation()).Connect(&Interface::HandleSignalPDU, this);
return true;
}
void Interface::Start()
{
// Get the DIS interface
mDisPtr = dynamic_cast<WsfDisInterface*>(&GetSimulation().GetExtension("dis_interface"));
}
Notes: In Interface::Start, we ask the simulation for the extension called “dis_interface”. This gives us a WsfSimulationExtension, which we cast to a WsfDisInterface.
In Interface::Initialize, we register for a callback. This callback gets triggered when a dis signal is received by the AFSIM Dis Interface. When this happens, we want to process it in Interface::HandleSignalPDU

## Slide 75: Exercise 3
Add member variables to class LocationMessage
Add Accessor/Mutator methods to class LocationMessage
Finish LocationMessage constructor
Complete SignalComm::Receive
Complete SignalComm::Send
Complete Interface::SendMessage
Complete Interface::HandleSignalPDU

## Slide 76: Comm Exercise 3 — Review 1
Review and understand the DataLink::Message class
  This class creates a datalink layer header for the LocationMessage data
  This class utilizes GenIO to serialize and de-serialize our data

## Slide 77: Comm Exercise 3 — Review 1 DataLinkMessage.hpp
class Message
{
public:
// This method reads enough of the input stream to
// determine the type of Message being read. It then creates the proper Message
// type from a factory class. Once the Message is generated,
// it is populated with the data from the input stream.
//
// The caller owns the returned Message and is responsible for its destruction.
static Message* Create(GenI& aGenI);
Message() = delete;
Message(const UtCalendar& aCurrentTime,
unsigned short aSourceTrackNumber);
explicit Message(GenI& aGenI);
virtual ~Message() noexcept = default;
enum Type
{
cUNDEFINED = 0,
cLOCATION = 1,
cNUM_MESSAGE_TYPES = 2
};

## Slide 78: Comm Exercise 3 — Review 1 DataLinkMessage.hpp
class Message
{
public:
// Input/output
virtual void Get(GenI& aGenI);
virtual void Put(GenO& aGenO) const;
virtual unsigned GetSize() const;
virtual int GetType() const { return cUNDEFINED; }
virtual const std::string& GetName() const;
virtual void TestData() const; // Test Message for bad or questionable data
// The following are simply the data and so are public
// Message header
unsigned short mSourceTrackNumber; // The originator of the message
unsigned short mSize; // total number of bytes in the Message
unsigned char mType; // Message type enumeration
unsigned char mHour; // 0-24 UT
unsigned char mMin; // 0-60
unsigned char mSec; // 0-60
};

## Slide 79: Comm Exercise 3 — Review 2
Review and understand the DataLink::LocationMessage class
  This class creates a datalink layer message for the LocationMessage class data
  This class also utilizes GenIO to serialize and de-serialize our data

## Slide 80: Comm Exercise 3 — Review 2 DataLinkLocationMessage.hpp
class LocationMessage : public Message
{
public:
LocationMessage() = delete;
LocationMessage(const UtCalendar& aCurrentTime,
unsigned short aSourceTrackNumber);
LocationMessage(const Message& aMessage,
GenI& aGenI);
~LocationMessage() noexcept override = default;
double mLatitude;
double mLongitude;
double mAltitude;
double mCourse;
double mSpeed;
unsigned GetSize() const override;
int GetType() const override { return Message::cLOCATION; }
const std::string& GetName() const override;
void Get(GenI& aGenI) override;
void Put(GenO& aGenO) const override;
protected:
virtual void GetMemberData(GenI& aGenI);
};

## Slide 81: Comm Exercise 3 — Review 3
WsfControlMessage.hpp and WsfStatusMessage.hpp already declare two types of messages used in this exercise
  WsfControlMessage: utilized by platforms that are commanders to send the “I COMMAND YOU” messages
  WsfStatusMessage: utilized by subordinates (those platforms with a commander) to send the “OK” messages back in response
This exercise adds a new type of message called LocationMessage
Inspect the LocationMessage.hpp file to become familiar with the class methods and attributes. Notice the new message type LocationMessage has been sub-classed from WsfMessage.

## Slide 82: Comm Exercise 3 — Review 3 LocationMessage.hpp
class LocationMessage : public WsfMessage
{
public:
LocationMessage();
...
int GetSourceTrackNumber() const { return mSourceTrackNumber; }
void SetSourceTrackNumber(int aSourceTrackId) { mSourceTrackNumber = aSourceTrackId; }
double GetLatitude() const { return mLatitude; }
void SetLatitude(double aLatitude) { mLatitude = aLatitude; }
...
double GetAltitude() const { return mAltitude; }
void SetAltitude(double aAltitude) { mAltitude = aAltitude; }
...
const char* GetScriptClassName() const override;
private:
int mSourceTrackNumber;
double mLatitude;
double mLongitude;
double mAltitude;
...
};

## Slide 83: Comm Exercise 3 — Task 1
Add private member variables to the LocationMessage class to store the following:
  The platform’s course (a double)
  The platform’s speed (a double)

## Slide 84: Comm Exercise 3 — Task 1 Solution LocationMessage.hpp
class LocationMessage : public WsfMessage
{
public:
LocationMessage();
...
private:
int mSourceTrackNumber;
double mLatitude;
double mLongitude;
double mAltitude;
// EXERCISE 3 TASK 1
double mCourse;
double mSpeed;
};

## Slide 85: Comm Exercise 3 — Task 2
Task 2: Provide public accessor and mutator functions similar in syntax to the other member variable’s accessors/mutators. These functions should be named:
  GetCourse
  SetCourse
  GetSpeed
  SetSpeed

## Slide 86: Comm Exercise 3 — Task 2 Solution LocationMessage.hpp
class LocationMessage : public WsfMessage
{
public:
LocationMessage();
...
// EXERCISE 3 TASK 2
double GetCourse() const { return mCourse; }
void SetCourse(double aCourse) { mCourse = aCourse; }
double GetSpeed() const { return mSpeed; }
void SetSpeed(double aSpeed) { mSpeed = aSpeed; }
const char* GetScriptClassName() const override;
private:
int mSourceTrackNumber;
double mLatitude;
double mLongitude;
double mAltitude;
// EXERCISE 3 TASK 1
double mCourse;
double mSpeed;
};

## Slide 87: Comm Exercise 3 — Task 3
Complete the LocationMessage class constructor implementation:
  Task 3a: Add the new member variables defined in the previous step to the constructor member initialization list and provide appropriate default values
  Task 3b: In the body of the constructor, set the message data using information from the originator of the message
    location (mLatitiude, mLongitude, mAltitude),
    course (which can obtained from the velocity by using atan2)
      Get the velocity
      Create a double array, velNED, of size 3, initialized to all 0.0s
      Invoke aPlatformPtr->GetVelocityNED(velNED)
      Invoke atan2(velNED[1], velNED[0]) and set the course equal to the result
    and speed
      Invoke aPlatformPtr->GetSpeed() and set the speed equal to the result

## Slide 88: Comm Exercise 3 — Task 3 Solution LocationMessage.cpp
LocationMessage::LocationMessage(WsfPlatform* aPlatformPtr)
: WsfMessage(GetTypeId(), nullptr, aPlatformPtr),
mSourceTrackNumber(0),
mLatitude(0.0),
mLongitude(0.0),
mAltitude(0.0),
// EXERCISE 3 TASK 3a
mCourse(0.0),
mSpeed(0.0)
{
// Set the source track number
mSourceTrackNumber = aPlatformPtr->GetAuxData().GetInt("SOURCE_TRACK_NUMBER");
// EXERCISE 3 TASK 3b
// Get location
aPlatformPtr->GetLocationLLA(mLatitude, mLongitude, mAltitude);
// Get course
double velNED[3] = { 0.0 };
aPlatformPtr->GetVelocityNED(velNED);
mCourse = atan2(velNED[1], velNED[0]);
// Get speed
mSpeed = aPlatformPtr->GetSpeed();
}

## Slide 89: Comm Exercise 3 — Review 4
Inspect the SignalComm.hpp file to become familiar with the class methods and attributes. Notice the new communication device type SignalComm has been sub-classed from wsf::comm::Comm.

## Slide 90: Comm Exercise 3 — Review 4 SignalComm.hpp
class SignalComm : public wsf::comm::Comm
{
public:
//! Constructor
explicit SignalComm(WsfScenario& aScenario);
SignalComm& operator=(const SignalComm&) = delete;
//! Virtual destructor
~SignalComm() noexcept override = default;
//! Get the class ID associated with the object (poor man's RTTI).
//! @return Returns the associated class ID.
static WsfStringId GetSignalCommClassId();
//! @name Framework methods
//@{
wsf::comm::Comm* Clone() const override;
bool ProcessInput(UtInput& aInput) override;
bool Initialize(double aSimTime) override;
//@}
unsigned int GetSourceTrackNumber() const { return mSourceTrackNumber; }
CommLab::Interface* GetInterface() const { return mInterfacePtr; }
bool Receive(double aSimTime, wsf::comm::Comm* aCommPtr, wsf::comm::Message& aMessage) override;
bool Send(double aSimTime, std::unique_ptr<WsfMessage> aMessagePtr, const Address& aAddress) override;

## Slide 91: Comm Exercise 3 — Review 4 SignalComm.hpp
void LocationMessageReceived(double aSimTime,
DataLink::LocationMessage* aLocMsgPtr);
const char* GetScriptClassName() const override;
protected:
//! Copy Constructor; used by clone
SignalComm(const SignalComm& aSrc) = default;
private:
unsigned int mSourceTrackNumber; //! Like a link-16 source identifier
CommLab::Interface* mInterfacePtr;
UtCallbackHolder mCallbacks;
};

## Slide 92: Comm Exercise 3 — Task 4
Implement SignalComm::Receive
  This method is called when a communication device is receiving a message
  Task 4a: Pass the message to the protocol stack
    Invoke mProtocolStack.Receive(aSimTime, aCommPtr, aMessage);
    Receive returns a bool, store this bool in the variable messageReceived
  Task 4b: Using the owning simulation object accessor, notify observers that a message has been received
    Invoking WsfObserver::MessageRecieved will generate the callbacks to the registered observers
    This is invoked as:
WsfObserver::MessageReceived(GetSimulation())(aSimTime, aCommPtr, this,
*aMessage.SourceMessage(), aMessage.GetResult());
  Task 4c: Send the message on to any on-board recipients
    Invoke the base class WsfPlatformPart::Send_Message method
      The arguments are
        the simulation time, and
        the aMessage parameter’s source message (obtained by invoking aMessage.SourceMessage()

## Slide 93: Comm Exercise 3 — Task 4 Solution SignalComm.cpp
bool SignalComm::Receive(double aSimTime, Comm* aCommPtr, Message& aMessage)
{
...
bool messageReceived = false;
// Perform a comm filter check
if (Component::Receive(*this, aSimTime, aCommPtr, aMessage))
{
// EXERCISE 3 TASK 4a
// Pass the message to the stack to see if it can be processed
messageReceived = mProtocolStack.Receive(aSimTime, aCommPtr, aMessage);
if (messageReceived)
{
// EXERCISE 3 TASK 4b
// Using the owning simulation object accessor,
// Notify simulation observers that a message has been received
WsfObserver::MessageReceived(GetSimulation())(aSimTime, aCommPtr, this,
*aMessage.SourceMessage(), aMessage.GetResult());
// EXERCISE 3 TASK 4c
// Forward the message to any on-board recipients (internal links)
SendMessage(aSimTime, *aMessage.SourceMessage());
}
//! Only throw a notification of message discarded if the message was intended for us and failed.
if (!messageReceived && aMessage.SourceMessage()->GetDstAddr() == GetAddress())
{
// This message is specifically for a protocol stack failure
WsfObserver::MessageDiscarded(GetSimulation())(aSimTime, aCommPtr,
*aMessage.SourceMessage(), "layer_receive_failure");
}
}
return messageReceived;
}

## Slide 94: Comm Exercise 3 — Task 5
Implement SignalComm::Send
  Note that this method is overridden from the base class wsf::comm::Comm
  We are not going to queue or route the message; when a message is sent it is immediately received
  Task 5a: Using the owning simulation accessor, notify observers that a message has been transmitted
    This is done as follows:
    WsfObserver::MessageTransmitted(GetSimulation())(aSimTime,this, *message.SourceMessage());
  Task 5b: Pass the message to the protocol stack, by executing:
  mProtocolStack.Send(aSimTime, message);
  Task 5c: Using the CommLab::Interface attribute, send the message over DIS, by executing:
  mInterfacePtr->SendMessage(aSimTime, GetPlatform(),
  mSourceTrackNumber, message.SourceMessage());

## Slide 95: Comm Exercise 3 — Task 5 Solution SignalComm.cpp
bool SignalComm::Send(double aSimTime, std::unique_ptr<WsfMessage> aMessagePtr,
const Address& aAddress)
{
...
// Perform a comm filter check
if (Component::Send(*this, aSimTime, *aMessagePtr, aAddress))
{
//! This object is only valid in the scope of this method call, and will
//! deallocate upon returning. If any object (layer, event, etc.) in the
//! stack call chain requires an extended lifetime of this object, it is
//! their responsibility to create such an object and manage it.
Message message(std::move(aMessagePtr));
message.SourceMessage()->SetDstAddr(aAddress);
message.SourceMessage()->SetSrcAddr(GetAddress());
// Use properties from the message table
GetScenario().GetMessageTable()->SetMessageProp(GetTypeId(), *message.SourceMessage());
// EXERCISE 3 TASK 5a
// Using the owning simulation accessor, notify observers that a message has been transmitted
WsfObserver::MessageTransmitted(GetSimulation())(aSimTime, this, *message.SourceMessage());
// EXERCISE 3 TASK 5b
// Using our comm's protocol stack, send the message
messageSent = mProtocolStack.Send(aSimTime, message);
// EXERCISE 3 TASK 5c
// Using the CommLab::Interface attribute, send the message over DIS
mInterfacePtr->SendMessage(aSimTime, GetPlatform(), mSourceTrackNumber, message.SourceMessage());
}
return messageSent;
}

## Slide 96: Comm Exercise 3 — Task 6
Implement CommLab::Interface::SendMessage
  This method gets called by a couple of classes in our exercise
    The SignalComm::Send method calls this method when a message of any type is being sent
Use an if statement to ignore any non-LocationMessage types.
  Use the LocationMessage::GetTypeId method to retrieve the LocationMessage’s type id,
  Use aMessage::GetType to retrieve the message type stored in the message
  Check and compare the type against the type id, and if they are not the same, then simply return from this method

## Slide 97: Comm Exercise 3 — Task 6 Solution Interface.cpp
void Interface::SendMessage(double aSimTime,
WsfPlatform* aSenderPlatformPtr,
int aSourceTrackNumberOffset,
const WsfMessage* aMessagePtr)
{
// EXERCISE 3 TASK 6a
// Check for quick return if this message type is not a LocationMessage.
if (aMessagePtr->GetType() != LocationMessage::GetTypeId())
{
return;
}
...

## Slide 98: Comm Exercise 3 — Task 7
Notice the creation of a variable dlMsg of type DataLink::LocationMessage
Task 7a: Pack up header and data into the DIS Signal PDU
  create a GenMemIO object as the send buffer
    the constructor takes two arguments:
      type GenBuf::Native, and
      size of the message (use dlMsg.GetSize, which returns number of bytes in message)
  Use the dlMsg message’s Put method to pack the data into the buffer
    Put takes a single argument which is the GenMemIo buffer
Task 7b: Set the user data in the Signal PDU
  Invoke signalPduPtr->SetUserData
  Parameterize with the buffer’s contents (buffer.GetBuffer) and size of the message in bits (use dlMsg.GetSize and convert to number of bits)
Task 7c: Send using the DIS interface
  Using the pointer mDisPtr, invoke the interface’s PutPdu method
    Pass in the sim time (aSimTime), and the unique_ptr signalPduPtr that is moved to the PutPdu method

## Slide 99: Comm Exercise 3 — Task 7 Solution Interface.cpp
void Interface::SendMessage(double aSimTime,
WsfPlatform* aSenderPlatformPtr,
int aSourceTrackNumberOffset,
const WsfMessage* aMessagePtr)
{
...
if (mDisPtr != nullptr)
{
...
const LocationMessage* msgPtr = dynamic_cast<const LocationMessage*>(aMessagePtr);
if(msgPtr != nullptr)
{
DataLink::LocationMessage dlMsg(currentTime, sourceTrackOffset);
dlMsg.mSourceTrackNumber = msgPtr->GetSourceTrackNumber();
dlMsg.mLatitude = msgPtr->GetLatitude(); dlMsg.mLongitude = msgPtr->GetLongitude();
dlMsg.mAltitude = msgPtr->GetAltitude();
dlMsg.mCourse = msgPtr->GetCourse();
dlMsg.mSpeed = msgPtr->GetSpeed();
// EXERCISE 3 TASK 7a
GenMemIO buffer(GenBuf::Native, dlMsg.GetSize());
dlMsg.Put(buffer);
// EXERCISE 3 TASK 7b
signalPduPtr->SetUserData(buffer.GetBuffer(), dlMsg.GetSize() * 8);
// EXERCISE 3 TASK 7c
mDisPtr->PutPdu(aSimTime, std::move(signalPduPtr));
}

## Slide 100: Comm Exercise 3 — Task 8
Implement CommLab::Interface:::HandleSignalPDU
This method is called when a Signal PDU is received by the DIS interface class
Task 8a: Process Signal PDUs only from a data link of type WsfDisSignal::EtGenericIP
  Use the PDU’s GetTDLType to check against this value
Unpack the DataLink::LocationMessage object from the DIS Signal PDU.
  Task 8b: Use a GenMemIO object that accesses the data buffer from the DIS Signal PDU
    Parameterize with:
      the signal data (call the signalData.data method),
      size of the buffer (dataLength)
      type (with type GenBuf::Native)
      and length of the data in the buffer (also dataLength)
  Task 8c: Utilize the DataLink::Message::Create factory method to read the DataLink::LocationMessge from the buffer
    Pass in the buffer into the Create method
    The return value is DataLink::Message* pointer and should be stored in a variable of that type (note: this variable must be named msgPtr, as this variable is used in later code that is provided for you)

## Slide 101: Comm Exercise 3 — Task 8 Solution Interface.cpp
void Interface::HandleSignalPDU(WsfDisInterface* aInterfacePtr, const WsfDisSignal& aPdu)
{
// EXERCISE 3 TASK 8a
// Use the PDUs GetTDLType() to check that it is of type
// WsfDisSignal::EtGenericIP, and if so return
if (aPdu.GetTDLType() != WsfDisSignal::EtGenericIP)
{
return;
}
if (mDisPtr != nullptr) // Must be configured with optional DIS interface
{
...
// EXERCISE 3 TASK 8b
// Use a GenMemIO object that accesses the data buffer from the DIS Signal PDU
// Parameterize with the signal data, type with type GenBuf::Native and length of the data
GenMemIO buffer(signalData.data(), dataLength, GenBuf::Native, dataLength);
// EXERCISE 3 TASK 8c
// Utilize the DataLink::Message::Create factory method to read the
// DataLink::LocationMessage from the buffer
DataLink::Message* msgPtr = DataLink::Message::Create(buffer);
...
}
}

## Slide 102: Exercise 4
Add UT_DECLARE_SCRIPT_METHOD macros to the ScriptLocationMessageClass for the new script methods Course and Speed
Add UT_DEFINE_SCRIPT_METHOD macros to LocationMessage.cpp for the new script methods Course and Speed
Add AddMethod calls to the ScriptLocationMessageClas constructor for the new script methods Course and Speed

## Slide 103: Comm Exercise 4 — Review 1 LocationMessage.hpp
Inspect the LocationMessage.hpp file to become familiar with the class methods and attributes of the ScriptLocationMessageClass class that is defined at the bottom of the file
Notice the new script message class ScriptLocationMessageClass has been sub-classed from WsfScriptMessageClass
class ScriptLocationMessageClass : public WsfScriptMessageClass
{
public:
ScriptLocationMessageClass(const std::string& aClassName,
UtScriptTypes* aScriptTypePtr);
void* Create(const UtScriptContext& aContext) override;
void* Clone(void* aObjectPtr) override;
void Destroy(void* aObjectPtr) override;
UT_DECLARE_SCRIPT_METHOD(SourceTrackNumber);
UT_DECLARE_SCRIPT_METHOD(Latitude);
UT_DECLARE_SCRIPT_METHOD(Longitude);
UT_DECLARE_SCRIPT_METHOD(Altitude);
};

## Slide 104: Comm Exercise 4 — Task 1
Declarations of script methods
  #define UT_DECLARE_SCRIPT_METHOD( … )
    Expands to a class declaration for method argument
    Inherits from class UtScriptClass::InterfaceMethod
    Declares constructor and operator() for the class’s methods
Task 1: Add a UT_DECLARE_SCRIPT_METHOD to the ScriptLocationMessageClass that declares a script called Course and another script called Speed. These methods allow access of the message contents in script.

## Slide 105: Comm Exercise 4 — Task 1 Solution LocationMessage.hpp
class ScriptLocationMessageClass : public WsfScriptMessageClass
{
public:
ScriptLocationMessageClass(const std::string& aClassName,
UtScriptTypes* aScriptTypePtr);
void* Create(const UtScriptContext& aContext) override;
void* Clone(void* aObjectPtr) override;
void Destroy(void* aObjectPtr) override;
UT_DECLARE_SCRIPT_METHOD(SourceTrackNumber);
UT_DECLARE_SCRIPT_METHOD(Latitude);
UT_DECLARE_SCRIPT_METHOD(Longitude);
UT_DECLARE_SCRIPT_METHOD(Altitude);
// EXERCISE 4 TASK 1
UT_DECLARE_SCRIPT_METHOD(Course);
UT_DECLARE_SCRIPT_METHOD(Speed);
};

## Slide 106: Comm Exercise 4 — Task 2
In LocationMessage.cpp, complete the implementation of the ScriptLocationMessageClass constructor
  Add calls to AddMethod for the Course and Speed script methods (similar to those for SourceTrackNumber, Latitude, Longitude, and Altitutde)

## Slide 107: Comm Exercise 4 — Task 2 Solution LocationMessage.cpp
ScriptLocationMessageClass::ScriptLocationMessageClass(const std::string& aClassName,
UtScriptTypes* aScriptTypesPtr)
: WsfScriptMessageClass(aClassName, aScriptTypesPtr)
{
SetClassName("LocationMessage");
mConstructible = true;
mCloneable = true;
AddMethod(ut::make_unique<SourceTrackNumber>());
AddMethod(ut::make_unique<Latitude>());
AddMethod(ut::make_unique<Longitude>());
AddMethod(ut::make_unique<Altitude>());
// EXERCISE 4 TASK 2
// add calls to AddMethod for the script methods Course and Speed
AddMethod(ut::make_unique<Course>());
AddMethod(ut::make_unique<Speed>());
}

## Slide 108: Comm Exercise 4 — Task 3
Definitions of script methods
  #define UT_DEFINE_SCRIPT_METHOD( … )
    Creates the class definition for the same “method” defined with the UT_DECLARE_SCRIPT_METHOD macro
    Also, expands to a sequence of C++ statements that creates a function whose body is the defined code for the macro
      This function is called from the operator() declared for the class
    Once defined, this script method can be called from the scripting interface in the scenario files
Task 3: Complete the implementation of the Course and Speed script methods at the bottom of the LocationMessage.cpp file.
  Remember, you must invoked the macro UT_DEFINE_SCRIPT_METHOD
  UT_DEFINE_SCRIPT_METHOD( … ) takes the following input arguments:
    Class: the class derived from UtScriptClass
    Obj_Type: the type of the application object
    Method: the name of the script
    Num_Args: the number of input arguments
    Ret_Type: a string indicating the type of the return value
    Arg_Types: a string with a comma separated set of types indicating the types of each of the input arguments (if there are no input arguments, this string should be the empty string)

## Slide 109: Comm Exercise 4 — Task 3 Solution LocationMessage.cpp
// EXERCISE 4 TASK 3a
UT_DEFINE_SCRIPT_METHOD(ScriptLocationMessageClass, LocationMessage, Course, 0, "double", "")
{
aReturnVal.SetDouble(aObjectPtr->GetCourse() * UtMath::cDEG_PER_RAD);
}
// EXERCISE 4 TASK 3b
UT_DEFINE_SCRIPT_METHOD(ScriptLocationMessageClass, LocationMessage, Speed, 0, "double", "")
{
aReturnVal.SetDouble(aObjectPtr->GetSpeed());
}
UT_DEFINE_SCRIPT_METHOD(ScriptLocationMessageClass, LocationMessage, Altitude, 0, "double", "")
{
aReturnVal.SetDouble(aObjectPtr->GetAltitude());
}

## Slide 110: Testing
In Visual Studio
  Build the solution in release
  Build the INSTALL Project
In ..\comm\data, inspect then run the run_all.bat file
Linux: from the build directory, run:
$ cmake --build . --target all -- -j11
$ cmake --build . --target install -- -j11

## Slide 111: Testing
The program should be tested with two scenario files named comm_scenario1.txt and comm_scenario2.txt located in the “..\comm\data” folder (we will not be using the Wizard for this test).

## Slide 112: Testing
  Mystic will start from the run_all.bat file.
  Since the application is viewing a file that is being updated in real-time, it would be best to configure it for this purpose.
  In the preferences, set the “At Scenario End” option to “Extrapolate”
  Now Mystic will extrapolate when it is played beyond the latest received data from the simulation.